Riverstone Terminal New South Wales

Pollution Incident Response Management Plan (PIRMP)

| Rev No | Reviewer | Review Date |
| --- | --- | --- |
| Revision 6 | Craig Roberts | 9th September 2016 |
| Revision 7 | Kylie Green | 6th December 2017 |
| Revision 8 | Kylie Green | 11th December 2018 |

Table of Contents

1. Pollution incident response management plan (pirmp)	3

1.1 Purpose and background											    3

1.2 Scope													    3

2. Legislative requirements											    3

3. Terms and definitions											    3

3.1 Definitions of pollution incident										    3

4. Notification of a pollution incident									    4

4.1 What must be notified											    4

4.2 Responsibility to notify											    4

4.3 Emergency response											    4

4.4 Contaminated land											    4

5. Reference documentation										    4

6 Description of potential hazards - environmental concerns						    5

6.1 Inventory of potential pollutants									    5

7. Safety equipment												    5

8. Notification procedure and contact details								    5

8.1 Internal and external notification contact details							    6

8.2 Communicating with local community									    6

8.3 Immediate neighbours											    6

8.4 Minimising harm to persons on premises								    6

8.5 Actions to be taken during or immediately after pollution incident					    6

Annexures

Annex A:   Site Plan – Riverstone	7

Annex B:    Spill Kits	8

Annex C:   Emergency Procedures	9

Annex D: Training Module	16

Annex E:  mergency Telephone Numbers – Auscol NSW	17

# Pollution Incident Response Management Plan (PIRMP)

# 1.1 Purpose and Background

Under GrainCorp’s Emergency Management System, detailed emergency response procedure is already in place for the classification and management of incidents, across GrainCorp operational sites. Under the provisions of Part 3A 98B(2) of the Protection of the Environment Operations (General) Amendment (Pollution Incident Response Management Plans) Regulation 2012, to allow for the integration of requirements into existing plans in respect to pollution incident response, requirements under POEO legislation have been integrated into these existing plans where appropriate.

This document has been designed as a reference to existing emergency response plans and associated procedure.  It also details additional supplementary site specific information as required under the POEO legislation, in respect to the relevant Environment Protection Licence (EPL) holder.

1.2 Scope

This PIRMP covers GrainCorp’s Auscol (Riverstone) Terminal. This plan applies to all activities, products and services on the site over which Auscols has operational control.

2 Legislative Requirements

Specific legislative requirements for the development and implementation of this PIRMP are provided in the following table.

Part 5.7A of the Protection of the Environment Operations Act 1997 (POEO Act)

Part 5.7A of the Protection of the Environment Legislation Amendment Act 2011 (POELA Act)

The Protection of the Environment Operations (General) Amendment (Pollution Incident Response Management Plans) Regulation 2012

Environment Protection License (EPL) 2550

3 Terms and Definitions

3.1 Definition of a pollution incident

A pollution incident means an incident or set of circumstances during or as a consequence of which there is likely to be a leak, spill or other escape or deposit of a substance, as a result of which pollution has occurred, is occurring or is likely to occur. It includes an incident or set of circumstances in which a substance has been placed or disposed of on a premises, but it does not include an incident or set of circumstances involving only the emission of any noise.

| Abbreviation | Explanation |
| --- | --- |
| EPA | Environment Protection Authority |
| PIRMP | Pollution Incident Response Management Plan |
| POEO Act | Protection of the Environment Operations Act 1997 |
| POELA Act | Protection of the Environment Legislation Amendment Act 2011 |
| CLM Act | Contaminated Land Management Act 1997 |
| EPL | Environment Protection License |
| ERP | Emergency Response Plan |
| EMS | Environmental Management System |

4. Notification of a Pollution Incident

4.1 What must be notified

A pollution incident is required to be immediately notified if there is a risk of ‘material harm to the environment’, defined under section 147 of the POEO Act as:

- harm to the environment is material if:

- it involves actual or potential harm to the health or safety of human beings or to ecosystems that is not trivial, or

(ii)   it results in actual or potential loss or property damage or an amount, or amounts in aggregate, exceeding $10,000 (or such other amount as is prescribed by the regulations), and

- loss includes the reasonable costs and expenses that would be incurred in taking all reasonable and practicable measures to prevent, mitigate or make good harm to the environment.

4.2 Responsibility to notify

Under Section 148 of the POEO Act, the following people have a duty to notify a pollution incident occurring in the course of an activity that causes or threatens material harm to the environment:

- The person carrying on the activity;

- An employee or agent carrying on the activity;

- An employer carrying on the activity;

- The occupier of the premises where the incident occurs.

Once determined that the incident causes or threatens material harm to the environment, notification must be given immediately, ie. promptly and without delay, after the person becomes aware of the incident.

4.3 Emergency Response

If a pollution incident occurs, all necessary action should be taken to minimise the size and any adverse effects of the release. If the incident presents an immediate threat to human health or property, Fire and Rescue NSW, the NSW Police and the NSW Ambulance Service should be contacted first for emergency assistance (phone 000). The other response agencies must still be contacted after that to satisfy notification obligations.

4.4 Contaminated Land

Persons whose activities have contaminated land and owners of land who become aware, or ought reasonably to be aware, that the land has been contaminated must notify the EPA as soon as practicable after becoming aware of the contamination, if the contamination meets certain criteria. The duty to notify is a requirement under section 60 of the Contaminated Land Management Act 1997 (CLM Act).

5. Reference Documentation

The following existing internal plans and procedure documentation underpin this PIRMP.

Document

Terminal Emergency Plan

Terminal Environmental Plan

Incident Emergency Response Plans – Annex C

Incident Notification and Escalation Flow Chart

6.  Description of Potential Hazards Environmental Concerns Significant Aspects

An environmental hazard is a term for any situation or state of events which poses a threat to the surrounding environment. Incident types and associated hazards are detailed in Annex 3.

Other pre-emptive actions taken to minimise the likelihood of potential environmental hazards include:

- The implementation of a site-specific Environmental Management System (EMS);

- Onsite inductions for employees, contractors and suppliers;

- Monthly environmental inspections.

6.1 Inventory of Potential Pollutants

An inventory of all chemicals is maintained under the Business Management system, and audits are undertaken onsite. There are no underground storage facilities at the Riverstone Terminal site. Chemical storage locations are detailed on Appendix 1.

The Site Manifest details the products stored on site.

7.  Safety Equipment

Under GrainCorp’s Safety Management Program and ‘Zero Harm for Life’ campaign,  Personal Protection Equipment (PPE) requirements are in place for all Terminal Operations for all employees, contractors, visitors and transport operators. Minimum PPE includes high visibility clothing, enclosed footwear, hard hats and safety glasses. Other onsite safety-related equipment includes:

- Onsite safety sign-in and inductions for all employees, contractors and suppliers

- Gas monitoring meters where required;

- Alarm systems;

- Emergency stop/shut down and alarm points;

- Chemical wash stations/showers;

- Spill kits;

- Online MSDS Register;

- Appropriate process and chemical identification signage;

- First aid facility and kits;

- Restricted chemical access.

8. Notification Procedure and Contact Details

Incident notification is detailed under the following sections of existing ERPs. Refer to these procedures to determine what information is required to be immediately reported to authorities in the event of a pollution incident.

If, under application of internal incident classification procedures, an environmental incident is determined to have caused or threatened material harm to the environment at the GrainCorp Riverstone site, the following internal and external stakeholders must be contacted immediately, in alignment with internal notification and escalation procedures.

Firstly, call 000 if the incident presents an immediate threat to human health or property. Fire and Rescue NSW, the NSW Police and the NSW Ambulance Service are the first responders, as they are responsible for controlling and containing incidents. If the incident does not require an initial combat agency, or once the 000 call has been made, notify the relevant authorities in the following order.

- the EPA

- the WorkCover Authority

- the local government authority

- Fire and Rescue NSW.

Complying with these notification requirements does not remove the need to comply with any other obligations for incident notification, for example, those that apply under other environment protection legislation or legislation administered by WorkCover.

8.1 Internal and External Notification Contact Details

Refer to  Annex E:   Emergency Telephone Numbers – Auscol NSW

8.2 Communicating with the Local Community

Communication and updates regarding pollution incidents will be undertaken in accordance with existing procedure as detailed in existing ERPs. provide information for communicating with neighbours and the local community, dependent upon the nature and scale of an incident. In the event of a notifiable incident, the appropriate emergency response plan and associated external communication process will be deployed.

8.3 Immediate Neighbours

In response to the introduction of changes to 5.7 of the POEO Act, and as part of this PIRMP, in the event of a notifiable pollution incident, and dependent upon nature and scale, immediate neighbouring properties will be notified, under the direction of Emergency Services with immediate response information.

8.4 Minimising harm to persons on premises

At all times minimising harm to persons shall be a priority. In addition to information provided detail of evacuation points are provided in, Appendix 1. Riverstone Terminal.

8.5 Actions to be taken during or immediately after a pollution incident

Internal incident management procedures, including the Notification and Escalation Flowcharts and   ERPs (Level One, Two and Three) provide detailed procedure as to immediate action to be undertaken during or immediately after an incident, dependent upon type and classification.

| Document | Reference |
| --- | --- |
| Incident Notification and Escalation Flow Chart | Complete Flowchart |
| Site Emergency Response Plan | Entire Plan |
| Site Terminal Emergency Plan | Entire Plan |

# Annexures

## Annex A:   Site Plan – Riverstone

## Annex B:    Spill Kits

While each terminal may have a different requirement for their specific site the fundamentals for spill control will designated by the Terminal Supervisor.  The Terminal Supervisor will be responsible for determining the following:-

- The type of material for the spill kit relative to the types of products stored e.g. flammable or Class 8,

- The quantity of spill kits to be used in a particular area of the site,

- The location of the spill kits in relation to site activities,

- The replenishment of used items within the spill kit,

- The amount of buffer stock on hand,

- Who is responsible for checking and reporting the status of the spill kits?

Spill Kit Contents

As a guide a general spill kit should contain the following items:-

Note: For dangerous goods refer to the class type for appropriate absorbent materials.

| 20 - 30 | 430x480mm Hazchem Absorbent Pad |
| --- | --- |
| 4 Bags | Absorbent material |
| 2 | 1.2m x 75mm Hazchem Absorbent Boom |
| 2 | 3m x 75mm Hazchem Absorbent Boom |
| 10 | Contaminated Waste Bags |
| 2 pair | Chemical Resistant Gloves |
| 1 Roll | Barrier tape. |
| 4 | Splash Goggles |
| 1 | 660L Mobile Bin |
| 1 Roll | Packing Tape |

Other practical tools to use with a spill kit.

- Squidgy for moving product and degreaser.

- Shovel for clean up.

- Broom for clean up.

- Buckets or pails for removal.

## Annex C:   Emergency Procedures

| EMERGENCY PROCEDURES General Instructions in the event of a: SPILL |
| --- |
| IF THIS HAPPENS: | DO THIS: |
| Small Spill or Leak (Less Than 20 Liters) | Shut down all operations in the vicinity of the spill/leak Try to locate and correct the source of the spill/leak Cover the spill with suitable absorbent material from spill kit. Ensure that you are wearing the correct PPE Remove the saturated absorbent to a safe place Record in incident log |
| Large Spill/Leak in the Terminal | Shut down all operations in the vicinity of the spill/leak Stop all road tanker and process operations as applicable Stop flow of product from source if possible Ensure bund valves are closed Ensure inlets to storm water interceptor is closed Immediately notify Terminal Supervisor of problem Terminal Supervisor is to assume the role of Incident Controller Incident Controller is to notify emergency services if assistance is required If required, prepare emergency equipment only if you are certain it is safe to do so. Assist in recovery of product as directed |
| Large Spill/Leak to the River | Shut down all operations in the vicinity of the spill/leak Stop all operations Stop flow of product from source if possible Immediately notify Terminal Supervisor of problem Terminal Supervisor assumes role of Incident Controller Incident Controller is to notify the General Manager and request assistance as required Incident Controller is to notify EPA Ph. 131 555 (02) 9995 5555 8. Assist in recovery of product as directed |
| General Environmental Controls Monitoring of Bund area valves and contents. Spill kit location for easy quick access at loading areas. Report any usage of spill kits for refilling. Appropriate PPE used for the products handled. Storm water valves to remain closed unless authorised to open by Supervisor. Report any incidents, near misses to Management for corrective action. Permit system to describe any special assessment requirements. Keep all drains and pits clear of debris. |

Annex C:   Emergency Procedures

| EMERGENCY PROCEDURES General Instructions in the event of Excessive Noise |
| --- |
| IF THIS HAPPENS: | DO THIS: |
| Extreme Excessive Noise | Immediate investigation of noise emission. If Safe to do so shut down offending operation / equipment Use hearing Protection to enter areas that have excessive noise levels. After shut down implement repairs, replacement or admin controls. Enter incident into SpheraCloud. |
| Complaints | Internal: Terminal Supervisor to investigate the source and implement corrective action. Follow up review with all staff as to the outcome. External: Terminal Supervisor to investigate the source and implement corrective action. Stop activity if due to breakdown and it is safe to do so. Inform the external parties of actions taken. Record any communications with external parties. Enter incident into the SpheraCloud. |
| General Controls for Noise. Elimination: Does the activity need to be done? Substitution: Can other equipment be used that has less noise emissions. Engineering: Modify or repair the equipment to an acceptable noise level. Administration: Control the timing of the operation to a time that has less impact on the community placement of any warning signs for operations. Monitoring of site operations with noise level tests. PPE : Issue appropriate hearing protection for areas of operation. Record findings in the incident log for any low level nuisance noise. For any excessive noise levels that need addressing put into SpheraCloud EPA Ph. 131 555 (02) 9995 5555 |

Annex C:   Emergency Procedures

| EMERGENCY PROCEDURES General Instructions in the event of AIR EMISSIONS |
| --- |
| IF THIS HAPPENS: | DO THIS: |
| Extreme Excessive Air, Dust, Smoke, Odours, Vapours | Immediate investigation of air emission. If Safe to do so shut down offending operation / equipment Use PPE – Appropriate respirator to enter areas that have excessive exposure levels. After shut down implement repairs, replacement or admin controls. Enter incident into the SpheraCloud. |
| Complaints | Internal: Terminal Supervisor to investigate the source and implement corrective action. Follow up review with all staff as to the outcome. External: Supervisor / Supervisor to investigate the source and implement corrective action. Stop activity if due to breakdown and it is safe to do so. Inform the external parties of actions taken. Record any communications with external parties. Enter incident into the SpheraCloud. |
| General Controls for Air Emissions: Elimination: Does the activity need to be done? Substitution: Can other equipment be used that has less noise emissions. Engineering: Modify or repair the equipment to an acceptable exposure level. Administration: Control the timing of the operation to a time that has less impact on the community placement of any warning signs for operations. Operators to have appropriate product training for potential leaks to atmosphere. Monitoring of site operations with air emission level tests for the appropriate release. PPE : Issue appropriate respirator protection for areas of operation. Record findings in the incident log for any low level air emissions. For any excessive emissions levels that need addressing put into SpheraCloud. EPA Ph. 131 555 (02) 9995 5555 |

Annex C:   Emergency Procedures

| EMERGENCY PROCEDURES General Instructions in the event of: Water Release |
| --- |
| IF THIS HAPPENS: | DO THIS: |
| Emergency Release of Storm Water | From rain buildup there may be a requirement for release of storm water to the environment. Management authority for release. Visual inspection of pit and drains prior to release. If clear and no residues on water then release to the environment. If not clear then remove any residues until clear then release. Check the outlet if available to confirm no contamination. Record open & close times and visual inspection times in the incident log book. Release and monitor at all time while the valve is open. Take a sample of the water released. Twice a year the sample must be tested externally for analysis. |
| Complaints | Internal: Terminal Supervisor to investigate the source and implement corrective action. Follow up review with all staff as to the outcome. External: Terminal Supervisor to investigate the source and implement corrective action. Stop activity if due to breakdown and it is safe to do so. Inform the external parties of actions taken. Record any communications with external parties. Enter incident into the SpheraCloud. |
| General Controls for Water Release: Rain water to be controlled for release by bunding for storage tank areas, loading areas and process areas. Contractor activities to identify soil erosion and run off to the environment. Storm water drains to signposted and locked with signage for Management Authorisation. Releases to the environment to be under full monitoring of the activity. Drains and gutters to be kept cleaned. Bund area reports to be actioned for any observations requiring improvements. Reuse rain water where practicable. EPA Ph. 131 555 (02) 9995 5555 |

Annex C:   Emergency Procedures

| EMERGENCY PROCEDURES GENERAL INSTRUCTIONS IN THE EVENT OF WASTE |
| --- |
| IF THIS HAPPENS: | DO THIS: |
| The waste generated at a Auscol site is in relation to the customer supplied products therefore as a result there is little produced by the terminal. It is a very low likelihood that an emergency will be initiated from a waste related incident.. |
| Waste release to the Environment | Immediate investigation of waste release. For general solid waste clean site for disposal. If Safe to do so use appropriate supplied container. Use PPE – to clean up then implement repairs, replacement or admin controls. Enter incident into SpheraCloud. All prescribed waste to be kept separate for licensed pick up and disposal. |
| Waste Controls | For General Waste: All waste to be place in containers that are appropriate for the type of waste. All containers to be kept closed to avoid pests, odours, and waste being blown out of the container. Waste tracking to confirm EPA Licensed approval. For Prescribed Waste: To be handled as per operating instructions. Oils, Fuels and Rags to be disposed of by EPA Licensed contractor. Customer supplied product waste under control of customer but also must be disposed of by licensed contractor. Waste tracking to confirm EPA Licensed approval. All documentation to be checked and records kept. |
| Recycling Avoid Reduce Reuse Recycle Recover Treatment and Disposal (Least Preferred) | Avoid printing of unnecessary documents/emails. Re-use the reverse side of paper. Separate paper/cardboard waste for recycling. Metal recycling by a metal recycler. Report any wastage to management for action. Keep records of waste amounts for disposal. Minimize the amount of energy usage by good supervision. EPA Ph. 131 555 (02) 9995 5555 |
| Annex C: Emergency Procedures |
| EMERGENCY PROCEDURES General Instructions In The Event Of A: TRANSPORT INCIDENT |
| IF THIS HAPPENS: | DO THIS: |
| Transport Incident Product Release | Immediately stop operation. Advise others by radio for assistance. If safe to do so contain the incident. Implement External Emergency Response for dangerous goods over 200ltrs. Close down vehicle access to the area. Use barriers to redirect traffic to other areas. Implement appropriate emergency response procedure e.g. Spill, Emissions, Noise, Land etc. |
| Complaints | Internal: Terminal Supervisor to investigate the incident and implement corrective action. Implement recommendations from investigations. Follow up review with all staff as to the outcome. External: Stop the transport activity if it is safe to do so. Terminal Supervisor to investigate the Transport Incident and implement corrective action. Inform the external parties of actions taken. Record any communications with external parties. Inform customers if they are affected. Enter incident into SpheraCloud |
| General Controls for Transport Incident. Transport Driver inductions and where appropriate applicable training for the driver. Transport driver to wear appropriate PPE for the operation. Auscol vehicles to have a spill kit for emergency use. Road tanker inspections for product compatibility, signage, tanker safety compliance e.g. fall protection, no leaks, no visible damage, no breakdown during loading. Report any observations to the Manager / Supervisor for action on non compliance. Record findings in the incident log for any observations. Terminal Supervisor for issues that need addressing put into SpheraCloud. EPA Ph. 131 555 (02) 9995 5555 |

Annex C:   Emergency Procedures

| EMERGENCY PROCEDURES GENERAL INSTRUCTIONS IN THE EVENT OF A: SOIL CONTAMINATION |
| --- |
| IF THIS HAPPENS: | DO THIS: |
| Small Land Spill or Leak (Less Than 20 Liters) | Shut down all operations in the vicinity of the spill/leak Try to locate and correct the source of the spill/leak Cover the spill with suitable absorbent material from spill kit. Ensure that you are wearing the correct PPE Remove the saturated absorbent to a safe place Remove affected soil to waste facility. Record in incident log |
| Large Land Spill/Leak in the Terminal | Shut down all operations in the vicinity of the spill/leak Stop all road tanker and ship operations as applicable Stop flow of product from source if possible Ensure bund valves are closed Ensure inlets to storm water interceptor is closed Immediately notify Duty Officer or Terminal Supervisor of problem Duty Officer or Terminal Supervisor is to assume the role of Incident Controller Incident Controller is to notify emergency services if assistance is required If required, prepare fire fighting monitors for dousing of foam only if you are certain it is safe to do so. Assist in recovery of product as directed Remove affected soil to waste facility. |
| Large Land Spill/Leak to land and the River | Shut down all operations in the vicinity of the spill/leak Stop flow of product from source if possible Immediately notify Terminal Supervisor of problem Terminal Supervisor assumes role of Incident Controller Incident Controller is to notify Mutual Aid Group and request assistance as required Incident Controller is to notify. EPA Ph. 131 555 (02) 9995 5555 Assist in recovery of product as directed Remove affected soil to waste facility. |
| General Environmental Controls Monitoring of Bund area valves and contents. Spill kit location for easy quick access at loading areas. Report any usage of spill kits for refilling. Appropriate PPE used for the products handled. Storm water valves to remain closed unless authorised to open by Supervisor. Report any incidents, near misses to Management for corrective action. Permit system to describe any special assessment requirements. Keep all drains and pits clear of debris. |

## Annex D: Training Module

| Training Element | Relevant Section in this Plan | Competency Required |
| --- | --- | --- |
| Responsibilities for Environmental controls:- Manager Supervisors Operators | Sect 2 Responsibilities | Competency Assessment |
| Environmental concerns for:- Water, General waste, Noise, Air Emissions, Soil Contamination. | Sect 4 Environmental Concerns | Competency Assessment |
| Location of Terminal:- Drains, Strom water, Separator pits, Spill kits. | Site drawings Terminal inspection Terminal site maps where listed. | Competency Assessment. Practical description of location. |
| Authority and control of locked drains and valves. | Terminal Supervisor guidelines. Routine Activities | Competency Assessment |
| Management Strategy for:- Air, Water, Soil. | Sect. 6.0 Emissions | Competency Assessment |
| Action on spill response:- PPE correctly identified, Control of spill, Record of incident SpheraCloud | Product Safety Assessments Product Safety Cards MSDS SpheraCloud | Competency Assessment |
| Administration: Location of Environmental Plans Location of Emergency Plans | Terminal Emergency Plan Terminal Environmental Plan | Competency Assessment. Practical description of location. |

## Annex E:   Emergency Telephone Numbers – Auscol NSW

EMERGENCY SERVICES CONTACT

| Company Name | Phone Bus. Hours | After Hours | Facsimile Number |
| --- | --- | --- | --- |
| Fire, Police, Ambulance | 000 | 000 |  |
| State Emergency Service | 132 500 | 0242516111 |  |
| Company Doctor, Akbal Jamesheed | 02 9627 2135 |  |  |

NEIGHBOURING SITES AND COMMUNITY

| Company Name | Phone Bus. Hours | After Hours | Facsimile Number |
| --- | --- | --- | --- |
| The Fabrication Pty Ltd | 0438821839 | 0438821839 |  |
| Gas Supply | 132462 | 132334 | 1800 065 420 |
| Electricity Origin | 1300658783 |  | 1800 065 420 |
| Water CWW | 132090 |  | 1300 362 092 |
| EPA | (02) 9995 5555 | 131 555 | 02 9995 5999 |
| Work cover | 13 10 50 |  | 1300 651 387 |
| Hawkesbury Council | 02 45604444 |  | 02 4587 7740 |

AUSCOL CUSTOMER CONTACTS

| Company Name |  | After Hours | Facsimile Number |
| --- | --- | --- | --- |

AUSCOL STAFF CONTACTS

| Name | Position | Phone Bus Hours | After Hours |
| --- | --- | --- | --- |
| Phil Neville | General Manager |  | 0427 086 466 |
| Kylie Green | Terminal Supervisor |  | 0437 926 125 |

# Text boxes

Loftus Street